U.S. Army Corps of Engineers, Pittsburgh                                                              July 14, 2010

Operations Division

MEMORANDUM FOR WATERWAYS ASSOCIATION OF PITTSBURGH

SUBJECT: July 2010 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS

The Pittsburgh District Repair Fleet is currently working at Montgomery L/D, on the Ohio River, to make lift gate repairs.  They will be working until 23 July 2010.  The large chamber will remain open and the small chamber will be closed intermittently.  There may be slight delays to navigation.

The District Repair Party is currently working at Lock #3 Mon River to replace deteriorated hydraulic lines.  This work will continue through 23 July 2010.  There may be slight delays to navigation.

The Pittsburgh District Repair Fleet will be dewatering the small chamber at Braddock L/D, Mon River from 2 August 2010 through 3 September 2010.  There will be slight delays to navigation.

The Pittsburgh District Repair Fleet will be dewatering the only chamber at Lock #2 Allegheny River.  There will be a complete closure of Lock #2 Allegheny River from 13 September 2010 through 27 September 2010 to complete gate seal and miter sill work.

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a. Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:  http://wmw.lrp.usace.army.mil

c. District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

The Turnpike Bridge over the Allegheny River was successfully dropped at 1000 yesterday, JULY 13, 2010.  The channel should be open by noon today.

The Change of Command Ceremony for Colonel Crall and Colonel Graham will take place at the Heinz History Center on Friday July 16, 2010 at 1030.

Walsh Construction, Contractor for Pennsylvania Turnpike will be constructing a four-lane concrete box girder bridge supported by two river piers constructed from causeways, over the Monongahela River at about Mile 59.1 near Denbo (Vesta No. 6), Washington County, Pennsylvania.  Navigational clearance during construction will be about 345 feet.  The work will be performed from 7:00 a.m. to 5:00 p.m. Monday through Friday beginning Monday, March 2, 2009 and ending February 7, 2011.  During this work, the M/V Okan Express provided by Ed McGavin would move the 40-foot x 50-foot, 7-foot draft Shugart Barge floating plant mounting a Reed SK 35 truck-mounted drill rig. The plant will include an 18-foot Skiff boat for safety.

Notice is hereby given that the USACE – Pittsburgh District will no longer send Notices to Navigation Interests by e-mail.  In order to view these notices, you must access the USACE – Pittsburgh District web page at www.lrp.usace.army.mil/or/or-f/navrpt.htm.

USACE will continue to send electronic version of Notices to Navigation Interests to USCG (United States Coast Guard) and the Waterways Association.

/signed/

RICHARD C. LOCKWOOD

Chief, Operations Division

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. of Pittsburgh Meeting 7/14/10

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

Weather became more summer-like with areas of thunderstorms producing varied amounts of rainfall across the region.  The most concentrated period of rain was from 2-6 June.  The heaviest rain fell in the Beaver and Ohio River basins.   Very little rain fell after 10 June and rivers were in a gradual recession through the end of June.

Temperatures were above normal. The majority of the rainfall in June occurred in the first nine days of the month. Rainfall averaged about 3.5 – 4.0 inches in the Allegheny and Monongahela River basins or about 0.75 of an inch below normal.  In the upper Ohio River basin rainfall was near normal averaging about 4.0 inches

At the Pittsburgh International Airport monthly precipitation was 5.13 inches, which is 1.01 inches above normal. Temperature averaged 2.5 degrees per day above normal. Rainfall for the year is 20.39 inches or 1.22 inches above normal.

For the first 13 days of July temperatures were 2.0 degrees/day above normal and rainfall was 1.83 inches which is 0.10 inches above normal.  Rainfall for the year is 22.22 inches or 1.19 inches above normal.

### RIVER FLOWS

Rainfall of 2.0 – 4.0 inches on 2 June resulted in rises of 2-3 feet on the Monongahela and Allegheny Rivers, and 3 – 7 feet on the Ohio River.  The more widespread nature of the rain on 5 Jun produced rises from 6-10 June of 2-3 feet on the Allegheny River, 3-4 feet on the Monongahela River, and 3-6 feet on the Ohio River.

#### HIGH WATER POTENTIAL

The high water potential is normal. Flows are currently 60% of normal on the Allegheny River, 125% of normal on the Monongahela, and 120% of normal on the Ohio River.   Rainfall of 2.0 – 2.5 inches in 6-12 hours is needed to bring rivers to bank full.

##### WEATHER FORECAST

Today.	Becoming partly sunny. Highs in the mid 80s. Northwest winds 5 to 10 mph.

Tonight. Partly cloudy in the evening, then becoming mostly clear. Lows in the mid 60s. Winds becoming light and variable late.

Thursday. Mostly sunny, hot and humid. Highs around 90. Southwest winds around 5 mph.

Thursday night. Partly Cloudy and humid with lows in the upper 60s. Southwest winds around 5 mph.

Friday.  Partly sunny in the morning, then becoming mostly cloudy with a 40 percent chance of showers and thunderstorms. Humid with highs in the mid 80s. Southwest winds 5 to 10 mph.

Friday night and Saturday. Mostly cloudy and humid with a 40 percent chance of showers and thunderstorms. Lows in the upper 60s. Highs in the mid 80s.

Saturday night. Mostly cloudy with a 30 percent chance of showers and thunderstorms in the evening. Lows in the mid 60s.

Sunday and Sunday night. Mostly cloudy with highs in the mid 80s and lows in the mid 60s

Monday through Tuesday. Partly cloudy. High in the upper 80s. Lows in the upper 60s.

8-14 Day Outlook…40 percent chance of above normal temperatures and near normal rainfall.

Jul Outlook...Near normal temperature and rainfall.

Jul-Aug-Sep Outlook…near normal temperature and rainfall.