U.S. Army Corps of Engineers, Pittsburgh                                                         14 November 2007

Operations Division

MEMORANDUM FOR WATERWAYS ASSOCIATION OF PITTSBURGH

SUBJECT:  November 2007 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 31 December 2007.

Montgomery L/D, Ohio River-  The U.S. Army Corps of Engineers' Repair Fleet is replacing the 13-ft x 14-ft land wall filling and emptying valves and renovating their operating machinery in the 110-ft x 600-ft lock chamber.  Work began on 29 October 2007 and is expected to be complete by 11:00 P.M. on 16 November 2007.  The Repair Fleet is staging the work from the small chamber thus closing the 56-ft x 360-ft lock chamber during the 19-day work period.  The large 110-ft x 600-ft lock chamber is open to navigation during this work period except that large chamber closures of up to 4-hours will occur periodically to install valve parts and equipment on the land wall.  See Notice to Navigation Interests No. 07-25.

Pike Island L/D, Ohio River-  The U.S. Army Corps of Engineers' Repair Fleet will replace the land wall filling tainter valve and renovate the operating machinery in the 110-ft x 600-ft lock chamber.  Work is scheduled to begin on 26 November 2007 and be complete on 14 December 2007.  The small 110-ft x 600-ft lock chamber will be closed to navigation during this work period.  The large 110-ft x 1200-ft lock chamber will be open to river traffic.  See Notice to Navigation Interests No. 07-28.

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a.   Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b.   Current River Conditions:  http://wmw.lrp.usace.army.mil

c.   District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

- Navigation Notice No. 07-34 containing the Repair Schedule for 2008 and 2009 was issued on 6 November 2007.  A Special Thanks goes out to the Waterways Association for their dedicated assistance in developing the 2-year repair schedule.

James J. Rockovich, P.E.

for  RICHARD C. LOCKWOOD

Chief, Operations Division

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. of Pittsburgh Meeting 11/14/07

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

Overall temperatures in October were well above normal with temperatures ranging from the upper 70s to upper 80s during the first week of the month.  Rainfall was slightly below normal in West Virginia, Pennsylvania, and Maryland and slightly above normal in Ohio.  Most of the rain in October occurred from 23rd to the 25th.  Rainfall averaged 2.0 – 2.5 inches or from near normal to 0.50 of an inch below normal in the Allegheny, Monongahela, and Ohio River basins and about 3.00 inches or 0.50 of an inch above normal in the Muskingum River basin.

At the Pittsburgh International Airport monthly precipitation was 1.70 inches, which is 0.55 of an inch below normal. Temperature averaged 6.8 degrees/day above normal.  Since 1 January precipitation has been 33.30 inches or 0.35 of an inch above normal.

For the first 13 days of November temperatures were 2.4 degrees/day below normal and precipitation was 1.19 inches which is 0.04 of an inch below normal.

### RIVER FLOWS

At the beginning of October seven day average flows were near normal and generally remained near normal throughout the month. Following the 23 - 25 October rain event, the Allegheny and Monongahela Rivers rose 1 – 3 feet, and rises on the Ohio River were less than 2 feet.

#### HIGH WATER POTENTIAL

The high water potential is below normal. Flows are near normal on the Allegheny and Ohio Rivers and 50 to 90 percent of normal on the Monongahela River. A widespread  2.0 to 2.5 inches of rain in 6 to 12 hours will bring rivers to bankfull.  The PA DEP continued the Drought Watch several counties in western Pennsylvania.

##### WEATHER FORECAST

Today:  60% chance of showers. High in the lower 60s.

Tonight:  60% chance of showers. Low in the upper 30s.

Thursday:  30% chance of afternoon showers. High in the lower 40s.

Thursday Night:  30% chance of evening rain/snow showers. Low near 30.

Friday:  Mostly cloudy. High near 40.

Friday Night:  Mostly cloudy. Low in the upper 20s.

Saturday:  40% chance of afternoon rain showers. High near 45.

Saturday Night: 40%chance of rain/snow showers. Low in the lower 30s.

Sunday:  Mostly cloudy. High near 45.

Monday:  Mostly cloudy.  Low in the lower 30s. High in the upper 40s.

Tuesday: Mostly cloudy.  Low near 35. High in the upper 40s.

8-14 Day Outlook…below normal temperature and above normal precipitation.

Nov Outlook...near normal temperature with near normal flows

Dec-Jan-Feb Outlook… above normal temperature and near normal flows.