U.S. Army Corps of Engineers, Pittsburgh

Operations Division

MEMORANDUM FOR:  Waterways Association of Pittsburgh

SUBJECT: Items of Interest to Navigation, September 12, 2013

- LOCK CLOSURES AND DELAYS

Ohio River

- Hannibal L/D, Pike Island L/D, New Cumberland L/D – Intermittent closures up to 4 hours in duration may be experienced August 2013 through April 2014 while the interlock controls systems are replaced. Closures will be during daylight hours only. Reference: Navigation Notice 13-35.

- Montgomery L/D – The auxiliary 56’ x 360’ river lock chamber will be closed in order to perform structural repairs to the dam gate end frames. Work is scheduled to begin at 0100 2 DEC 2013 and end at approximately 2300 20 DEC 2013. Reference: Navigation Notice 13-34.

- Emsworth L/D – The primary 110’ x 600’ lock chamber will be closed in order to make repairs on the filling valves located on the upper end of the middle wall. Work is scheduled to begin at 0100 15 OCT 2013 and end at approximately 2300 22 NOV 2013. Reference: Navigation Notice 13-33.

2.  OTHER ITEMS OF INTEREST

Ohio River

- Emsworth L/D - Shoaling has been reported in the lower approach channel near the mouth of Lowries Run Creek. USACE is currently developing plans for the possible dredging of the area. Reference: Navigation Notice 13-37

Allegheny River

- L/D 5 - Shoaling has been reported in the lower approach channel. On 5 SEP 2103 an extensive hydrographic survey was conducted upstream and downstream of Locks 5 & 6 to identify scouring issues near the dam and to quantify dredging needs. Commercial tows are advised to modify their approach and exit angles in the downstream lock approach until the conditions are addressed. Reference: Navigation Notice 13-32.

- L/d 2 & CWBY – Due to infrastructure conditions and safety concerns, USACE will not assist deck hands with the placement of tow lines on the upper and lower guide walls EXCEPT in emergency situations until a new walking surface is constructed. Reference: Navigation notice 13-31.

Miscellaneous

- Notice is hereby given that the USACE Pittsburgh District will no longer send Notices to Navigation Interests by e-mail. USACE will continue to send electronic version of Notices to Navigation Interests to United States Coast Guard (USCG) and the Waterways Association. In order to view these notices, readers must access the USACE Pittsburgh District web page at:

http://www.lrp.usace.army.mil/missions/NavigationNotices.aspx

- River Navigation Charts are available by calling the Government Printing Office Book Store at 866-512-1800.

3.  RECOMMENDED INTERNET SITES

- Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

- Current River Conditions:  http://wmw.lrp.usace.army.mil

- District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

- LPMS Public Web Site:  http://corpslocks.usace.army.mil/

/signed/

KATHY M. GRIFFIN

Chief, Operations Division