U.S. Army Corps of Engineers, Pittsburgh                                                           9 April 2008

Operations Division

MEMORANDUM FOR WATERWAYS ASSOCIATION OF PITTSBURGH

SUBJECT:  April 2008 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 15 June 2008.

Hildebrand L/D, Monongahela River-  The U.S. Army Corps of Engineers' Repair Fleet started the dewatering job in the single 84-ft x 600-ft lock chamber to renovate the miter gates and seals on 31 March 2008.  Work is on schedule and is expected to continue through 25 April 2008.  The lock is closed to navigation during this 26-day work period.  (Reference Notice to Navigation Interests No. 08-03)

New Cumberland L/D, Ohio River-   The work scheduled for 10 April 2008 at New Cumberland Locks has been cancelled; there will not be a 10-hour closure of the locks as was originally planned.  High water on the Ohio River has delayed transportation of the three large absorber units to the First Energy (Ohio Edison) Sammis Plant.  Babcock & Wilcox Construction Company Inc. (under contract with FirstEnergy) has cancelled the unloading of three large absorber units by roll-off operation at the temporary unloading ramp along the right descending bank of the Ohio River within the downstream approach to the New Cumberland Locks and Dam.  This roll-off operation which was originally scheduled from 7:00 A.M. to 5:00 P.M. on

10 April 2008 is postponed to a future date.  A new navigation notice will be issued upon rescheduling this work activity.    (Reference Notice to Navigation Interests No. 08-08 REV)

Lock 2, Allegheny River-  The U.S. Army Corps of Engineers' Repair Fleet will replace the land wall emptying valve and renovate the operating machinery in the single 56-ft x 360-ft lock chamber.  Work is scheduled to begin on 6 May 2008 and will be completed on 23 May 2008.  The lock chamber will be open to river traffic; however, closures of 4 to 8 hours (approximately 5 times during the 18-day work period) will occur periodically to move and install valve parts and equipment on the land wall.  (Reference Notice to Navigation Interests No. 08-06)

Lock 4, Allegheny River-  The U.S. Army Corps of Engineers' Repair Fleet will renovate two filling and two emptying valves, and their operating machinery in the single 56-ft x 360-ft lock chamber.  Work is scheduled to begin on 27 May 2008 and will be completed on 13 June 2008.  The lock chamber will be open to river traffic; however, tows will be restricted to 52-feet wide during this 18-day work period.

U.S. Army Corps of Engineers, Pittsburgh                                                           9 April 2008

Operations Division

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a.   Daily Navigation Conditions:  www.lrd-wc.usace.army.mil/text/pitrpti.txt

b.   Current River Conditions:  http://wmw.lrp.usace.army.mil

c.   District Navigation Notices:  www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

- Inland Rivers Ports & Terminals, Inc. - Annual Conference is being held in New Orleans, Louisiana from 9-11 April 2008.

James J. Rockovich, P.E.

for RICHARD C. LOCKWOOD

Chief, Operations Division

2

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. of Pittsburgh Meeting 04/09/08

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

## WEATHER RECAP

Temperatures were below normal in March with plenty of rain. Precipitation was well above normal averaging 4.5 - 5.0 inches in the Allegheny, Monongahela, and Ohio River basins or 0.75 – 1.75 inches above normal. There were two large rises on 4-6 March and 18-21 March.  Smaller rises occurred on the Allegheny and Ohio Rivers on 14-16 March and 27-30 March. Rainfall of 1.0 – 1.5 inches on 3-4 was proceeded by a rapid snowmelt which started rivers rising before the rain occurred.

At the Pittsburgh International Airport monthly precipitation was 3.92 inches, which is 0.75 inches above normal. Temperature averaged 2.8 degrees/day below normal. The monthly snowfall was 4.7 inches or 3.2 inches below normal.

For the first 9 days of April temperatures were 3.8 degrees/day above normal and precipitation was 0.52 of an inch which is 0.28 of an inch below normal.  The seasonal snowfall total is 41.2 inches which is 1.3 inches above normal.

### RIVER FLOWS

On 4-6 March the Allegheny and Monongahela Rivers rose 4-7 feet and the Ohio River 12-13 feet. Minor rises of 2-3 feet occurred on the Allegheny and Ohio Rivers from 14-16 March, and on 27-30 March rises were  2-3 feet on the Allegheny River and 3-5 feet on the Ohio River.  Another widespread rain event of 0.75 to 1.5 inches on 18-19 March produced  rises of 4-7 feet on the Allegheny River, 4-9 feet on the Monongahela River, and 10-12 feet on the Ohio River.

#### HIGH WATER POTENTIAL

The high water potential is above normal. Currently flows are 125 - 150% of normal on the Allegheny River, and near normal on the Monongahela and Ohio Rivers. A storm will move through the area on Friday.  A widespread 1.5 to 2.0 inches of rain 6 to 12 hours will bring rivers to bankfull.

##### WEATHER FORECAST

Today: 30% chance of showers and isolated thunderstorms. High in the mid 60s.

Tonight:  30% chance of showers and isolated thunderstorms.  Low in the upper 40s.

Thursday:  Partly cloudy. High in the mid 60s

Thursday Night: Mostly cloudy.  Low in the lower 50s.

Friday:  60% chance of showers and thunderstorms. High around 70.

Friday Night:  60% chance of showers and possible thunderstorms. Low near 53.

Saturday:  Mostly cloudy.  50% chance of morning showers. High near 55.

Saturday Night: Mostly cloudy. 30% chance of showers. Low near 35.

Sunday:  Cloudy. 40% chance of rain/ snow showers. High near 45.

Monday:  Cloudy. 30% chance of rain/snow showers. Low near 35. High near 45.

Tuesday: Partly cloudy. Low near 30. High in the upper 40s.

8-14 Day Outlook…below normal temperature and above normal precipitation.

Apr Outlook...near normal temperature with near normal flows on the Monongahela River and above normal on the Allegheny and Ohio Rivers

May-Jun-July Outlook…near normal temperature near normal flows.