U.S. Army Corps of Engineers, Pittsburgh                                                       12 April 2006

Operations Division

MEMORANDUM FOR Waterways Association of Pittsburgh

SUBJECT:  April 2006 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 30 June 2006.

Emsworth L/D, Ohio River-  The U.S. Army Corps of Engineers Repair Fleet is making repairs to the downstream land wall gate anchorage in the 110-ft x 600-ft lock chamber.  The repair job began on 10 April 2006 and is currently on schedule to be completed by 11:00 PM on 14 April 2006.  The 110-ft x 600-ft lock chamber will be closed to river traffic during this 5-day work period.  The 56-ft x 360-ft lock chamber will be open to navigation during this work period.  Major delays are expected.  (See Notice to Navigation Interests No. 06-6)

Hildebrand L/D, Monongahela River-  The U.S. Army Corps of Engineers Repair Fleet will dewater the single 84-ft x 600-ft lock chamber and repair the lock gates and seals.  The work is scheduled from 2 May 2006 through 2 June 2006.  No river traffic can pass through Hildebrand during this 32-day work period.  (See Notice to Navigation Interests No. 06-8)

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a. Daily Navigation Conditions:

www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:

wmw.lrp.usace.army.mil/current/

c. District Navigation Notices:

http://www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

As part of the Lower Mon River Project, five (5) dikes are to be constructed in the upstream approach to Braddock L/D, Mile 11.3, Monongahela River.  The Corps of Engineers investigated construction of these flow control dikes at the current intermediate pool elevation of El. 721.8

Operations Division

SUBJECT: April 2006 Meeting

and concluded that the dikes could be constructed at this intermediate pool level without any adverse hydraulic effects.  The tops of the stone dikes are to be constructed to El. 708.7 providing a freeboard of 13.1 feet over the top of the dikes at the current intermediate operating pool.  With consideration of allowable tolerance for stone placement underwater, we would expect to have no local high spots shallower than 12.5 feet at the intermediate operating pool level of El. 721.8.  This work, when complete, will mitigate outdrafts in the upstream approach

to the locks during high water events.  A contract was awarded to Eagle Design on 30 March 2006; the Notice to Proceed is anticipated to be issued on or before 20 April 2006.  The Contractor will be required to have a communication and coordination plan with navigation interests as well as a helper boat available to assist tows navigating the upper approach during the dike placement activities.

Other Pittsburgh District Activities.

o     COL Stephen L. Hill deployed on 5 March 2006 to support post Hurricane Katrina and Rita recovery efforts.  He will serve as the Mississippi Valley Division G3 Operations Officer located in New Orleans, LA and will focus on efforts to restore the levee system.  During his 2-month deployment, LTC Peter A. Steinig is the Acting Commander for the Pittsburgh District.

o     Richard Lockwood is on a special assignment throughout the month of April 2006 and has been tasked to lead the Pittsburgh District Asset Management Project Delivery.

o     Michael B. White, Director of Programs, and Bob Willis, Chief of Operations from the Great Lakes and Ohio River Division Office in Cincinnati, OH will be coming to Pittsburgh for a visit.  On Thursday, 13 April 2006, they will get an overview of the Allegheny River navigation system including making a visit to Lock 9, Lock 5 and possibly other facilities on the lower Allegheny River.  They want to understand our funding issues/concerns and meet with recreational and commercial stakeholders.

/signed/

JAMES J. ROCKOVICH, P.E.

Acting Chief, Operations Division

2

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. Of Pittsburgh Meeting 4/12/06

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.weather.gov/pittsburgh

WEATHER RECAP

March was a cool dry month with the only significant rainfall occurring on the 12th and 13th of the month.  The trend of below normal precipitation which, began in February, continued in March averaging 1.5 – 2.0 inches in the Allegheny, Monongahela, and Ohio River basins, which is 1.5 – 2.0 inches below normal.

At the Pittsburgh International Airport monthly precipitation was 2.12 inches, which is 1.05 inches below normal. Temperature averaged 1.6 degrees/day below normal. Snowfall was 1.4 inches, which is 6.5 inches below normal.

For the first 11days April temperatures were 1.0 degree above normal and precipitation was 0.90 of an inch or 0.2 of an inch below normal. Snowfall was 0.2 of an inch. Snowfall for the season is 32.2 inches or 8.0 inches below normal.

### RIVER FLOWS

At the beginning of March flows on the area’s rivers were at or below normal in the Allegheny, Ohio, and Monongahela River basins.  Following a general 1.0 – 1.5 inches of rainfall on 12 – 13 March, rivers rose throughout the region.  From 12 – 15 March the Allegheny and Monongahela Rivers rose 3 – 6 feet, the Ohio River rose 4 – 8 feet.  Rivers receded through the end of the month. Currently flows on the Allegheny, Monongahela, and Ohio Rivers are only 45 to 55 percent of the long term median flow

#### HIGH WATER POTENTIAL

The high water potential is below normal. Flows are low, particularly in the tributaries.  A widespread 2.0 to 2.5 inches of rain in 6 to 12 hours is needed to bring the major rivers to bankfull.  PA DEP has issued a Drought Watch for all of Pennsylvania.

WEATHER FORECAST

Today:  50% chance of showers and thunderstorms. High in the upper 60s

Tonight:  70% chance of showers and thunderstorms. Low in the lower 50s

Thursday: Partly cloudy. High in the lower 70s

Thursday Night: 50% chance of showers and thunderstorms.  Low in the lower 50s

Friday:   60% chance of showers and thunderstorms. High in the lower 70s

Friday night: Mostly cloudy. Low in the lower 50s

Saturday:  Partly cloudy. High near 70

Saturday Night:  Partly cloudy. Low in the upper 40s

Sunday:  Partly cloudy. 40% chance of showers.  High in the upper 60s

Monday:  40% chance of thunderstorms. Low near 45. High in the upper 60s

Tuesday:  Partly cloudy. Low near 45. High 65

The 8 to 14 day forecast…above normal temperatures and below normal precipitation.

The Apr Outlook …above normal temperature and below normal precipitation.

The May-Jun-Jul Outlook…near normal temperature and at or below normal                                                             precipitation.