U.S. Army Corps of Engineers, Pittsburgh                                                                 11 May 2005

Operations Division

MEMORANDUM FOR Waterways Association of Pittsburgh

SUBJECT:  May 2005 Meeting

##### ITEMS OF INTEREST TO NAVIGATION

1.  LOCK CLOSURES AND DELAYS - The following is the schedule of lock closures and delays through 30 September 2005.

a. Maxwell L/D, Monongahela River - The U.S. Army Corps of Engineers Repair Fleet closed and will dewater the 84-ft x 720-ft river lock chamber to repair the lock gates, sills, and gate anchorages.  Work began on 2 May 2005 and is scheduled to be complete by 15 June 2005.  The river lock chamber will be closed to navigation during the 45-day work period.  The 84-ft x 720-ft land lock chamber will be open to navigation interests with only minor delays expected.  (Reference Notice to Navigation Interests No. 05-2)

b. New Cumberland L/D, Ohio River - The U.S. Army Corps of Engineers Repair Fleet will close and dewater the small 110-ft x 600-ft lock chamber to (a) repair the lock gates, sills and gate anchorages; and (b) repair the service bridge lift span over the upstream end of the small chamber.  Work is scheduled to begin on 6 July 2005 and be complete by 2 September 2005.  The small chamber will be closed for this 59-day work period.  The large 110-ft x 1200-ft lock chamber will be open to navigation interests with only minor delays expected.  (Reference Notice to Navigation Interests No. 05-9)

2.  RECOMMENDED INTERNET SITES - The following sites are recommended for the most up-to-date navigation information.

a. Daily Navigation Conditions:

www.lrd-wc.usace.army.mil/text/pitrpti.txt

b. Current River Conditions:

wmw.lrp.usace.army.mil/current/

c. Pittsburgh District Navigation Notices:

www.lrp.usace.army.mil/or/or-f/navrpt.htm

3.  OTHER ITEMS OF INTEREST

Dredging of the lower approach at Emsworth L/D, Ohio River was completed on 29 April 2005.

Operations Division

SUBJECT:  May 2005 Meeting

A hydrographic survey (soundings) was taken of the area at approximate Mile 19.7, Monongahela River (at Peters Creek) to define the quantity of material to be removed.  Once the spoil material is characterized, a dredging contract will be awarded with dredging activity expected to start in the latter part of June 2005.

As part of the Lower Mon River Project, five (5) dikes are to be constructed in the upstream approach to Braddock L/D, Mile 11.3, Monongahela River.  The Corps of Engineers investigated construction of these flow control dikes at an intermediate pool elevation of El. 721.8 and

concluded that the dikes could be constructed at this intermediate pool level without any adverse hydraulic effects.  The tops of the stone dikes are to be constructed to El. 708.7 providing a freeboard of 13.1 feet over the top of the dikes at the current intermediate operating pool.  With consideration of allowable tolerance for stone placement underwater, we would expect to have no local high spots shallower than 12.5 feet at the intermediate operating pool level of El. 721.8.  This work, when complete, will mitigate outdrafts in the upstream approach to the locks during high water events.  It is anticipated that the dikes may be constructed in the October-December 2005 timeframe utilizing one 10-hour shift each day for approximately 2 months.  The Corps of Engineers contractor will be required to have a helper towboat available to assist tows navigating the upper approach during the 10-hour shift each day that dike placement activities are taking place.

RICHARD C. LOCKWOOD

Chief, Operations Division

2

# RIVER AND WEATHER CONDITIONS

Prepared for Waterways Assn. Of Pittsburgh Meeting 05/11/05

National Weather Service Forecast Office, Pittsburgh PA

For the latest river and weather forecasts--http://www.erh.noaa.gov/pbz

WEATHER RECAP

Rainy conditions during the first three days of the month produced stream and river rises during the first week of April.  This was followed by nearly two weeks of dry weather along with well above normal temperatures, and rivers receded to near normal levels.  April ended with a return to cold and rainy conditions for the last week and a half of the month with rivers climbing to above normal levels by month’s end.

At the Pittsburgh International Airport monthly precipitation was 3.72 inches, which is 0.71 of an inch above normal. Temperature averaged 2.3 degrees/day above normal.  Snowfall was 6.3 inches bringing the seasonal total to 49.5 inches, which is 8.9 inches above normal.

For the first 10 days of May temperatures have been 4.7 degrees/day below normal and precipitation was 0.21 of an inch or 0.93 of an inch below normal.

RIVER FLOWS

At the beginning of April flows were above normal. Following the rains during the first 3 days of April, the Allegheny River rose 2 - 4  feet, the Monongahela River about 1.5 feet, and the Ohio River 5 - 6 feet over several days. Rivers receded to near normal levels during the middle portion of the month, only to return to above normal flows by the end of April with rises of 1.5 – 2.5 feet on the Allegheny River, 2 – 3 feet on the Monongahela River, and 3.5 – 4.5 feet on the Ohio River.  Currently flows are near normal all major rivers.

HIGH WATER POTENTIAL

High water potential is near normal. Groundwater levels are high, but lowering and soils are very moist. Runoff potential is moderate.  A widespread 2.0 to 2.5 inches of rain in 6 to 12 hours is needed to bring the major rivers to bankfull. Currently, models are not indicating any excessive rainfall events.

WEATHER FORECAST

Today:  20 percent chance of late afternoon thunderstorms. High near 80.

Tonight:  Becoming mostly cloudy. A 50 percent chance of thunderstorms.  Low near 50.

Thursday: 30 percent chance of showers and thunderstorm in the morning…then partly cloudy.

High in the mid 60s.

Thursday Night:  Partly cloudy. Low in the upper 40s.

Friday:  Mostly cloudy with a 50 percent chance of showers and thunderstorms. High near 70.

Friday Night:  Mostly cloudy. A 50 percent chance of thunderstorms. Low in the upper 50s.

Saturday:  70 percent chance of showers and thunderstorms. High near 70.

Saturday Night:  50 percent chance of showers and thunderstorms.  Low near 50.

Sunday:  30 percent chance of showers. High 65 to 70.

Monday:  Partly cloudy. Low near 50. High near 70.

Tuesday:  Partly cloudy. Low near 50. High near 70.

The 8 to 14 day forecast is for below normal temperature and near normal rainfall.

The May Outlook is for below normal temperatures and rainfall.

The Jun-Jul-Aug Outlook is for near normal temperature and precipitation.